## Slide 1: Code Team Meeting #1: Commands And Subsystems
Date: 5/18/2023

## Slide 2: Agenda
Introductions
Post-Season Plans
What is Command-Based Programming?
What are Subsystems and Commands?
Where do we use them?
Practice

## Slide 3: Command-Based Programming
Using WPI Lib resources to code and instruct the robot
Command-Based Programming for FRC focuses on using Commands and Subsystems
Commands represent actions the robot can take
Subsystems are collections of robot hardware (motors, lights, camera, action, sensors) that are accessed by Commands

## Slide 4: Subsystems
Subsystems store a collection of robot hardware to be accessed by other code
Subsystems are “background commands”; they will run as a default when no other command is running
Generally, subsystems are where hardware is controlled
Key Method: public void periodic()

## Slide 5: Commands
Commands are the actions that a robot can take
A command accesses an instance subsystem to set conditions on the robot’s hardware
Key Methods: initialize(), end(), execute(), isFinished(), addRequirements()

## Slide 6: The RobotContainer & Robot Classes
The Robot class controls the flow of the code when the robot is running (there shouldn’t be much in this class)
The Robot class instantiates a RobotContainer object and creates the CommandScheduler that control robot commands
The RobotContainer class stores subsystems and commands and binds buttons to commands

## Slide 7: Examples From This Year
Subsystem: https://github.com/FRC5827/2023Private/blob/main/src/main/java/frc/robot/subsystems/FlapdexerSubsystem.java
Command: https://github.com/FRC5827/2023Private/blob/main/src/main/java/frc/robot/commands/FlapdexerCommand.java

## Slide 8: Useful Documents
FRC Explains Commands: https://docs.wpilib.org/en/stable/docs/software/commandbased/commands.html
FRC Explains Subsystems: https://docs.wpilib.org/en/stable/docs/software/commandbased/subsystems.html
FRC Explains how to set up a Command-Based Project: https://docs.wpilib.org/en/stable/docs/software/commandbased/structuring-command-based-project.html

## Slide 9: Try for next week…
Create a subsystem that would control a single motor and a command that has the motor rotate one revolution